## Slide 1
Real-Time Ball-Balancing Robot
Project: real-time ball-balancing robot using camera + STM32 + 3-leg RRS platform.
Goal: keep an orange ball centered on a circular platform by tilting it with three servos.
Main components: camera + OpenCV, Python sender, STM32 controller, PID loop, inverse kinematics, 3R-R-S mechanical legs.

## Slide 2
Mechanical Design
R-R-S Topology
Mechanism type: R-R-S topology (two revolute joints + spherical joint at the moving platform).
Leg Configuration
Each leg: base revolute actuated by a servo → link → spherical joint to the platform.
Platform Design
Platform: circular plate where ball rolls; base triangle provides three actuation points.
Design Goals
Key design goals: stiffness, safe servo travel (servoMin=40 to servoMax=120), and known neutral geometry for IK.
Figure1: revolute joint
Figure2: revolute & spherical joints
Figure0: The design of the system

## Slide 3
Hardware Implementation
Custom PCB
Custom PCB for signal & power routing.
Power System
Servos powered by an external 5 V adapter
Figure3: Final PCB
Figure4: Final PCB with the system
Figure5: Power supply adapters

## Slide 4
Computer Vision System
01
Color Detection
Color detection: convert frame to HSV, apply HSV range (default hsv_lower=[5,150,150], hsv_upper=[25,255,255]) to isolate orange pixels.
02
Shape Detection
Shape detection: blur mask (Gaussian 9×9) then use HoughCircles (dp=1.2, param1=100, param2=15, minRadius≈55–70) to find circular ball contour → returns (x,y,r).
03
Visualization & Calibration
Visualization & calibration: draw a constant blue border circle at (320,240) with adjustable border_radius (default 205) and a red center point at (320,240) to align camera pixels with the physical platform circle.
04
Data Transmission
Data transmission: when ball found, Python sends "x,y\n" over serial at up to 50 Hz (send interval 0.02 s). If not connected, the overlay shows "STM: Disconnected".
Figure8: Video of the final algorithm
Figure7: real time calibration window
Figure6: photo of the final algorithm

## Slide 5
STM and Serial Communication
Serial Link
Serial link: Python → STM32 over UART (example Python port COM23, baud 115200).
Data Format
Sent format: simple ASCII "x,y\n" (parser also accepts (x,y)), STM32 reads line-by-line.
Parsing
Parsing: STM32 trims newline, extracts x and y as floating values and updates lastSerialTime.
Status & fail-safe: if no serial updates for >500 ms, STM32 returns platform to flat (0,0). Also Python shows connection status overlay.

## Slide 6
SYSTEM MODILING
Collecting Data
Using the encoder built-in the Servo
Data Format
Time in ms, command in deg,, and measured deg from the encoder
using ID tools
Obtained the TS of the servo sing the black box method
Figure10: Data has been collected
Figure9: Servo abu_daneb
Figure11: Fitting the servo graph
Figure13: TS function of the servo
Figure12: Fitting the servo graph

## Slide 7
SYSTEM MODILING and Simulink
Figure14: Simulink file without IK
Figure15: scope of figure 14 system
Figure16: the Simulink of the final system
Figure17: scope of figure 16 system

## Slide 8
PID Control System
Pixel Error Definition
Pixel error definition: error = center - ball_pixel where centerX=320, centerY=240.
PID Implementation
PID implementation (discrete, sample time LOOP_PERIOD_MS = 20 ms):
integr += (err + err_prev) * dt (trapezoidal integration)
deriv = (err - err_prev) / dt
out = kp*err + ki*integr + kd*deriv
Control Parameters
Gains used in code: kp = 0.00030, ki = 0.0, kd = 0.00020 (units: output slope per pixel).
Safety Constraints
Saturation & safety: PID outputs are constrained to [-maxSlope, +maxSlope] with maxSlope = 0.9 to limit platform tilt.
Control loop: if new sample available, compute PID and call moveTo(platformHz, -out_x, -out_y) at 50 Hz.

## Slide 9
Inverse Kinematics
Definition
What is IK: algorithm that converts desired platform pose (height + tilt slopes) into required actuator joint angles for each leg.
Implementation
In our implementation: we use machine.theta(legIndex, hz, nx, ny) which returns the required theta for each leg given platform height platformHz and slopes (nx, ny).
Servo Mapping
From theta → servo angle: servoAngle = servoNeutral + servoSign * round(theta - theta0) where theta0 is baseline flat theta.
Control Flow
Safety & mapping: resulting servo angles are constrained to safe travel [servoMin, servoMax] and then written to servos.
Overall flow: pixel coords → PID → slopes (nx,ny) → IK (thetaA,B,C) → servo angles → actuation.
Figure18: simple explanation of the IK
Figure19: IK final equations